## Slide 1: SECS: Efficient Deep Stream Processing via Class Skew Dichotomy

## Slide 2: Outline
Motivation
Class skew
Efficient utilizing class skew: probability layer
Class skew dichotomy
Class-specific pruning

## Slide 3: Image processing on emerging mobile platforms
Heavy resource consumption on energy and memory
Robotics
Glasses

## Slide 4: Existing approaches
Model Pruning
  Network quantization: 5x speed up, 7.1% less accuracy
  Filter pruning: 4x less computation, 2.81% less accuracy
Existing approaches all trade accuracy for less resource consumption
On-device scheduling
  Dynamically select smaller model according to runtime resource budget
  4x less latency, 4% less accuracy.
Notes: Resnet 18

## Slide 5: Our approach: Class skew
Definition: a few classes appear in an environment, while others appear seldomly or does not appear at all.
  Through one year: thousands of people
  In lab: less than ten people
Both reduce resource consumption and increase accuracy

## Slide 6: Basic example: class skew
Through one year: thousands of people
In lab: less than ten people
Less classes required in lab
Need a small model with 10 classes
Replace the complex model with 1000 classes
Less classes means
Higher accuracy
Less resource consumption
Notes: Make left one look like the right one

## Slide 7: Efficiently utilize runtime class skew
Our approach: An efficient model adaption approach that can adapt model without any overhead during runtime.
Existing approach: Reduce number of nodes in the last layer and finetune the last few layers.
Challenge: Class skew may switch frequently as time goes, i.e., every 5 minutes. However, existing approaches would take at least 14 seconds latency or even minutes, as well as lots of computation.

## Slide 8: Efficiently utilize runtime class skew: probability layer
An extra layer after the original model.
Only need to modify parameters in the last layer.
No overhead is introduced.

## Slide 9: Further observation: class skew dichotomy
Hot class skew appear frequently in the future
Cold class skew never appear again
Inspired by techniques from source code optimization, two modes are designed for hot/cold class skew.
Interpretation for cold class skew: efficient adaption during runtime with probability layer
Compilation for hot class skew: aggressive optimization on the model by class-specific pruning.

## Slide 10: Class-specific pruning: motivation
Some classes are easier to distinguish while others are hard
Small models for simple classes and complex models for hard ones

## Slide 11: Class-specific pruning: perforation
Different class skew requires different model architecture.
Small models for simple classes and complex models for hard ones
Automatically decide the hyperparameters, i.e., layer, channel, neurons.
Challenge: Retraining is required for every new hyperparameter.
Our solution: Use perforation to recover the feature maps size to enable the forward computation.
  Generate a sequence of models with increasing accuracy without any finetune.

## Slide 12: SECS Architecture
Profiler for detecting class skew
Probability layer for efficient model adaption during runtime
Perforation for class-specific pruning